## Slide 1: ME729 Advanced Robotics - Singularity and Motion Trajectories
2/26/2018
Sangsin Park, Ph.D.

## Slide 2: Singularity
Kinematic singularities
  The inverse mapping from Cartesian space to joint space is not sometimes defined.
  Those positions of the robot are referred to as singularities or degeneracies.
  At a singularity,
    Infinite inverse kinematic solutions may exist.
    Small Cartesian motions may require infinite joint velocities.
  Boundary Singularities (also known as workspace singularities)
    Usually caused by a full extension of a joint.
  Internal Singularities (also known as joint space singularities)
    Caused by an alignment of the robots axes in space.
  By analyzing the Jacobian matrix of a manipulator, we can find the singular positions of the robot.
Joint space
Cartesian space
Inverse kinematics

## Slide 3: Singularity
Finding singularities of the 2-link manipulator
  If we invert the Jacobian, we get .
  The inverse is undefined whenever ; It is a singular matrix.
  So, by solving , we can find singularities in the robot workspace.
  , where and are constant.
  If , the manipulator is at full extension (), or looped back onto link 1 ().
To remind formula for determining the inverse of 2x2 matrix.
If , then
.

## Slide 4: Motion Trajectories
Why do we need them?
  A set of desired angles are determined by application of the inverse kinematics.
  During the last lab, we’ve just sent desired angles to motors as a reference input.
  These references are step inputs and have problems.
  If at , it’s a step input and discontinuous at .
  So, Its velocity becomes impulse.
    It consumes the high current suddenly.
    It makes a jerk motion.
    It makes the system broken.
Step input
Impulse velocity

## Slide 5: Motion Trajectories
To make trajectories smooth
  A simple way is to connect both by a linear function.
    Its velocity also has discontinuous points at boundaries.
  We should design a trajectory which has at least zero velocities at boundaries.  Cubic polynomials
  I recommend that a trajectory has zero velocities and accelerations at boundaries.  Quintic polynomials

## Slide 6: Motion Trajectories
Cubic polynomials
  Two constraints on the function’s value come from the selection of initial and final values:
  An additional two constraints are that the function is continuous in velocity, which in this case means that the initial and final velocity are zero:
  These four constraints can be satisfied by a polynomial of at least third degree.
  And the four coefficients are determined by the four constraints.
Solving these equations for the ,

## Slide 7: Motion Trajectories
Quintic polynomials
  The first four constraints are same as cubic polynomials’ those
  An additional two constraints are that the function is continuous in acceleration, which in this case means that the initial and final acceleration are zero:
  These six constraints can be satisfied by a polynomial of fifth degree.
  And the all coefficients are determined by the six constraints.
Solving these equations for the ,
, ,

## Slide 8: Motion Trajectories
The way to implement motion trajectories
  We need to discretize continuous trajectories with a sampling frequency.
  and , where .
  And then, we set the sampled points to reference input sequentially.
  So, we need a timer to discretize and update reference input in real-time.
Sampling frequency : (: period)