## Slide 1
Automata: Putting it all together
© Copyright Paul Oh

## Slide 2
18:00 Guest Lecture
18:30 Lab “Putting it All Together”: Automata example (The Gymnast)
19:15 Project Time: Form (2-3 person) team; Automata sites and concept sketches
20:00 Email Team Proposal (3-slides: inspirational video and sketches)
20:15 Clean up and Adjourn
Tentative Schedule
© Copyright Paul Oh

## Slide 3
Review
Lab 1: Simple Machine I: Levers, Shafts, And Cranks
Simple Crank
Crank 3-bar
Crankshaft
Complex Crank
Hands-on Lab
Homework
Constructed slider-crank mechanism
Lab 2: Simple Machine II: Cams, Springs, And Linkages
Cam Follower
Cam Follower Vehicle
Torsional Linkage
Multi-jointed Torsional Linkage
4-bar linkage walker
Hands-on Lab
Homework
Flat folding chair
Lab 3: Simple Machine III: Ratchets, Drives, And Gearing
Planetary Gears
Bevel Gears (and Pin Wheel)
Worm Gears
Rack-and-Pinion
Hands-on Lab
Homework
Windshield Wiper
Complexity Level
Result is a cookbook with fundamental
recipes. Now, you can create a meal
© Copyright Paul Oh

## Slide 4
http://www.youtube.com/watch?v=zy5B_bzNlD4
Input: handle crank (Lab 1)
Follower pushes ratchet (Lab 3)
Cam and follower (Lab 2)
Conversion of translation to stepped rotation
Detent prevents ratchet 2 from reversing
Output: multi-link figure rotates
Lego-based Automata – The Gymnast
Video
© Copyright Paul Oh

## Slide 5
Cam Follower
(Lab 2)
Drive Train
(Lab 3)
Pin Wheel
(Lab 3)
Crank Handle
(Lab 1)
Figure is Linkage
(Figure 03)
Drive Train
(Lab 3)
Ratchet
With Detent
(Lab 3)
Spring
(Lab 2)
© Copyright Paul Oh

## Slide 6
Lego-Based Automata: The Gymnast
Step 1: Assemble rails
2x Brick 1x16
3703
2x Brick 1x6
3894
2x Beam 5
3216
4x Pin With Friction
4459
2x Plate 1x4
3710
Connect the 2 bricks with a plate. Secure connection with a beam. Construct 2 of these
© Copyright Paul Oh

## Slide 7
Step 2: Assembly Gear Train
2x Gear 24T
3648
2x Axle Pin
3749
Gear 40T
3649
Axle Towball 2736
Bush 3713
Cross Block 1x3
32184
Axle 5 3705
Align and insert first 24T Gear. Mesh and insert 40T Gear. Align second 24T gear and thread
Axle-5. Secure with bush and attached cross block. Insert Axle Towball in cross block
© Copyright Paul Oh

## Slide 8
Step 3: Construct the gymnast figure
2x Beam 3x5
Bent 90
(32526)
Beam 7 (32524)
2x Beam 2x4 Liftarm Bent 90 (32140)
Cross Block 1x3 with 4 pins (48989)
2x Pin Long (32556)
Axle 4 (3705)
2x Bush 1/2 Type 1
(4265A)
Create upper body by inserting long pins in
Beam 7. Create arms by attaching 2x4 liftarms.
Create lower body by connecting 3x5 beams to
cross block. Attach lower and upper bodies
with axle. Secure with1/2 bushes
© Copyright Paul Oh

## Slide 9
Step 4: Attach gymnast to rails
2x Gear 4 Knob (32072)
Gear 8T (3647)
Beam 3x0.5 Liftarm (33299)
2x Axle 10 (3737)
Align and thread Axle 10 through gymnast. Secure with 4 knob.
Align and thread Axle 10 at rail bottom. Mesh 8T gear. Secure at end with 3x0.5 liftarm (handle)
© Copyright Paul Oh

## Slide 10
Step 5
Beam 2x4 Liftarm Bent 90 (32140)
Axle Towball 2736
Cross Block 1x3
(32184)
Bush 1/2 Type 1
(4265A)
Bush 3713
Axle 4 (3705)
Plate 2x8
(3034)
Construct detent by threading Axle 4 through
2x4 liftarm. Secure with 1/2 bush and cross block.
Attach towball to cross block. Secure rails with
plate. Secure crank axle with bush.
Beam 3x5 Bent 90
(32526)
Pin Long (32556)
2x Pin With Friction
(4459)
A rubber band will be used for the detent.
Attach the 3x5 liftarm to top of rail. Rubber
band will be looped to towball and long pin
© Copyright Paul Oh

## Slide 11
Step 6
4x Plate 2x8
(3034)
2x Brick 1x6
(3894)
6x Brick 1x2
(3004)
Rubber Band
Use 2x8 plates to secure rails at top and bottom. Brace 1x6 bricks at bottom of rail
structure. Use 1x2 bricks to complete brace. Loop rubber band at towball and 3x5 liftarm
© Copyright Paul Oh

## Slide 12
Step 7
2x Brick 1x8
with holes
(3702)
Secure 1x8 bricks at underneath rails (towards bottom)
© Copyright Paul Oh

## Slide 13
19:15 Project Time: Form 2-3 person team. Automata sites and concept sketches
Automata Project
NB: Project counts towards 25% to 35% of final grade
Grading Criteria:
Automata must consist of at least 2 simpler mechanisms e.g. crank and ratchet
Must be only Lego pieces (can self-purchase extra parts if needed)
Option to work on a 2-3 person team
15%: Brief explanation of how automata works
15%: Video (20-seconds) compares role model and your creation
25%: MLCAD Build instructions including Bill of Materials
25%: Step-by-step build instructions (photo-based). Bring hardcopy to class next week
20%: Oral Presentation (5-min) showcasing the 4 points above
20:15 Email Team Proposal (3-slides: inspirational video and sketches)
Web search for Automata that you’d like (and have parts) to reproduce
  Slide: results of web search
Concept sketches
  Slide: scan of concept sketches
Prototypes: some possible reproductions in Lego
  Slide: Photos of reproductions, MLCAD constructions
© Copyright Paul Oh