## Slide 1
H-Bridges
© Copyright Paul Oh, 2007, Rich Vallett 2011; Updated 2016

## Slide 2: H-Bridges
Circuits that uses switches to reverse the direction of the current
Vcc
M
+
Vcc
M
+
Vcc
M
+
Vcc
M
+
Circuit is open; motor is free to rotate in either direction
Diagonal switches (top right, bottom left) are closed; motor spins in positive (CCW) direction
Diagonal switches (top left, bottom right) are closed; motor spins in negative (CW) direction
Bottom switches are closed; motor terminals are grounded, which stops motor

## Slide 3: Direction Control (Transistor H-Bridges)
Action | B3 | B2 | B1 | B0
Free rotation | 1 | 0 | 1 | 0
Forward | 1 | 1 | 0 | 0
Backward | 0 | 0 | 1 | 1
Brake | 1 | 1 | 1 | 1
C
B
E
Vcc
1kΩ
E
B
C
B3
C
B
E
E
B
C
1kΩ
B2
1kΩ
B1
1kΩ
B0
M
+
+
C
B
E
Vcc
1kΩ
E
B
C
B3
C
B
E
E
B
C
M
1kΩ
B2
1kΩ
B1
1kΩ
B0
Transistors act as electronic switches which can be controlled by the digital output of a microcontroller and can direct the flow of current in the circuit with little current applied to the base of each transistor
http://www.robotroom.com/BipolarHBridge.html

## Slide 4: Lab
Brushed DC Motor Control
  Building and controlling a brushed DC motor using an H-bridge circuit and the NXT Sensor Expansion Kit

## Slide 5: Transistor H-Bridge
Part | Name | Value
Resistor | R1 | 1kΩ
 | R2 | 1kΩ
 | R3 | 1kΩ
 | R4 | 1kΩ
Transistor | T1 | PNP
 | T2 | PNP
 | T3 | NPN
 | T4 | NPN
Diode | D1 | Power
 | D2 | Power
 | D3 | Power
 | D4 | Power
Motor | M1 | Brushed
Battery | P1 | 9V
C
B
E
P1
R1
E
B
C
B3
C
B
E
E
B
C
R3
B2
R2
B1
R4
B0
M
+
T1
T2
T4
T3
M1
D1
D2
D3
D4

## Slide 6: Lab Setup
9V Battery and plug
Brushed DC motor
Wire holder
NXT
H-Bridge
Proto-board

## Slide 7: Circuit
9V Battery and plug
Connect the proto-board GND pin to common ground
Bridge both power and ground rails
PNP
NPN

## Slide 8: Output
Press the center button □ to let the motor spin freely
Press the right button > to drive the motor backward
Press the left button < to drive the motor forward