## Slide 1
legoCameraTowerBuildInstructions-041220a
Copyright (c) 2020, Paul Oh
Lego-based USB Camera Tower Build Instructions

## Slide 2
legoCameraTowerBuildInstructions-041220a
Copyright (c) 2020, Paul Oh
3708 Axle 12
3708 Axle 8
6538
Axle Joiner
32064 1x2 Brick
with Axlehole
3713 Bush
4265c
1/2 Bush
30517 2 x 2 x 10 Girder
Triangular Vertical
Step 1: Gather Parts
Step 2: Attach Axle-12 to Axel Joiner. Insert Axle-8 to Axle and Pin Connector triple
Step 3: Slide 2 Bushes to both left and right ends of Axle-8
Step 4: Slide half-bush and connect with Axle-12 thru Axle Joiner. Attach two 1x2 Bricks to Tower (NB: orientation of Brick’s Axle hole and Tower)
63869 Axle and Pin Connector Perpendicular Triple

## Slide 3
legoCameraTowerBuildInstructions-041220a
Copyright (c) 2020, Paul Oh
Step 5: Attach two 1x2 Bricks to remaining tower. Align Axel holes with left and right Axle-12 parts (see inset photo)
Step 6: Gather Parts. Spinel 2MP full HD USB Camera Module (640x480) FOV 100 degrees Amazon
Step 7: Screw M2.5 Bolt into Washer and Beam 5 and secure with Nut. NB: Camera orientation and mounting hole locations (2 views above given)
Step 8: Screw remaining M2.5 Bolt
M2.5 Bolt-12
M2.5 Washer
M2.5 Nuts
2780 Friction Pegs
32316 Beam-5
USB Camera Module
Mounting holes
USB Connector Cable

## Slide 4
legoCameraTowerBuildInstructions-041220a
Copyright (c) 2020, Paul Oh
Step 9: Attach 2 Friction Pegs into Beam 5
Step 10: Attach Beam 5 to Axle and Pin Connector Triple. NB: Camera orientation (inset photo)
Step 11: Note spacing (2 right photos) and mount Tower to Base Plate. Gather parts
4282
Plate 2x16
15397 Cross (Black)
4073 Plate Round 1x1
(Black and Green)
32x32 Base Plate
(White)

## Slide 5
legoCameraTowerBuildInstructions-041220a
Copyright (c) 2020, Paul Oh
Step 12: Affix 2x16 Plate across two 2x16 plates. Place 1x1 Round in center
Step 13: Attach 2x16 plates to Tower. NB: Camera orientation.
Step 14: Attach Black Cross (somewhere near arm) and Black Round 1x1 plates at top left and right corners
Note how camera’s lens is centered on the 2x16 Beam (as indicated by Green 1x1 Rounds)
Congratulations! Completed construction of a Lego Camera Tower

## Slide 6
legoCameraTowerBuildInstructions-041220a
Copyright (c) 2020, Paul Oh
Completed Lego Camera Tower overlooking 2-DOF planar manipulator
Stack of 17 Technic Bricks between Base Plate and Lens. 17 x 6 mm + 1 mm (due to stud) = 103 mm distance