## Slide 1
Step A: Truss Sub-Assembly
Step A-1: Lower Truss
2x 15-Beam 32278
2x
7-Beam 32524
4x Pin 3L with Stop Bush 32054
4th hole
Gather parts (left). Insert two Pin 3L at each end of 7-Beam. Repeat with other 7-Beam. Connect 7-Beams to 4th hole of 15-Beam. Finished step (right)
1x 11-Beam 32525
4x 3-Axle 4519
Gather parts (left). Insert a 3-Axle in each Pin 3L’s Stop Bush. Lay 11-Beam diagonally across 3-Axles. Finished step (right)
Close-up of Finished step

## Slide 2
2x 7-Beam 32524
4x Pin 3L with Stop Bush 32054
Gather parts (left). Insert each Pin 3L Stop Bush over the 3-Axle. Connect 7-Beam over each Pin 3L. Finished step (right)
Close-up of Finished step
2x 15-Beam 32278
4x 5-Beam 32316
8x Friction Pin 2780
Gather parts (left). Connect 15-Beams over Pin 3L. Connect 5-Beam to 15-Beam with Friction Pins Finished step (right)
Close-up: Red arrows show where Friction Pins are inserted into 15-Beam and 5-Beam. The remaining 6 Friction Pins are also seen

## Slide 3
Close-up of Finished brace. Red arrows point to locations of Friction Pins to connect 5-Beams to 15-Beams
Completed Lower Truss

## Slide 4
Step A-2: Middle Truss
2x 15-Beam 32278
2x 7-Beam 32524
4x Pin 3L with Stop Bush 32054
Gather parts (left). Insert two Pin 3L at each end of 7-Beam. Repeat with other 7-Beam. Connect 7-Beams to 3rd and 5th holes of 15-Beam. Finished step (right)
5th hole of 15-beam
3rd hole of 15-beam
Close-up of finished step
1x 11-Beam
32525
4x 3-Axle 4519
Gather parts (left). Insert each 3-Axle into each Pin 3L’s Stop Bush. Diagonally lay11-Beam over Axles
Close-up of finished step

## Slide 5
2x 7-Beam 32524
4x Pin 3L with Stop Bush 32054
Gather parts (left). Insert each Pin 3L’s Stop Bush into 3-Axle. Insert 7-Beam over Pin 3L peg. Finished step (right)
Close-up: Red Arrows show a Pin 3L’s Stop Bush inserted over a 3-Axle.
Close-up: 7-Beam inserted into Ping 3L

## Slide 6
2x 15-Beam 32278
Gather parts (left). Insert 15-Beam over Pin 3L pegs. Finished step (right)
Completed Middle Truss
(NB: Has 4 open holes in 15-Beam)
4 open holes

## Slide 7
Step A-3: Upper Truss
2x 13-Beam 41239
2x 7-Beam 32524
4x Pin 3L with Stop Bush 32054
Gather parts (left). Insert two Pin 3L at each end of 7-Beam. Repeat with other 7-Beam. Connect 7-Beams to 2nd and 4th holes of 13-Beam. Finished step (right)
Close-up: Red Arrows show Pin 3L inserted into 2nd and 4th holes of 13-Beam
4th hole of 13-Beam
2nd hole of 13-Beam

## Slide 8
1x 11-Beam 32525
4x 3-Axle 4519
Gather parts (left). Insert 3-Axles into Pin 3L’s Stop Bush. Lay 11-Beam diagonally across. Finished step (right)
2x 7-Beam 32524
4x Pin 3L with Stop Bush 32054
Gather parts (left). Insert Pin 3L’s Stop Bush onto 3-Axles. Insert 7-Beams onto Pin 3L’s pins. Finished step (right)
2x 13-Beam 41239
Gather parts (left). Insert 13-Beams over Pin 3L’s pins. Finished step (right)
Completed Upper Truss

## Slide 9
Step A-4: Lower-to-Middle Truss Connection
Middle Truss
Lower Truss
8x Friction Pin 2780
Gather parts Lower (Step A-1) and Middle (Step A-2) trusses. Note the orientation (red arrows) of diagonal braces
Insert friction pins. Top 4 red down-arrows show a completed connection. Bottom 2 red up-arrows show friction pins exposed. Note orientation of diagonal braces
Flip over. 15-Beams removed to make connection easier. Note orientation of diagonal braces
Completed Lower-to-Middle Truss Connection
Lower-to-Middle Truss Connection

## Slide 10
Step A-5: Upper Truss Connection
4x 5-Beam 32316
16x Friction Pin 2780
Lower-to-Middle Truss Connection
Upper Truss
Gather Lower-to-Middle Truss Connection (Step A-4). Bottom assembly: Goal is to connect Upper Truss (Step A-3) to the Lower-to-Middle Truss Connection. Note: Red arrows show diagonal orientation
Insert 8 Friction Pins (red arrows) and use 5-Beam to attach Upper Truss to the Lower-to-Middle Truss Connection
Flip over. Insert 4 friction pins
Connect 5-Beam. Flip over. Insert remaining 4 friction pins.
5-Beam attached

## Slide 11
Step B-1: Angle Mount
8x Friction Pin 2780
Completed 3-stage Truss (Step A-5)
2x Axle Pin 43093
2x Long Pin 6558
2x 3x5 Liftarm 32526
2x 1x2 Beam Pin and Axle Hole 60483
2x 7-Beam 32524
1x 4 Pin 3L Connector 48989
Gather Parts and the Completed Truss (from Step A-5)
Hi Technic Angle Sensor https://www.hitechnic.com/cgi-bin/commerce.cgi?preadd=action&key=NAA1030
Step B: Angle Sensor Sub-assembly
Insert Long Pin in Angle Sensor Mount. Attach 1x2 Beam Pin and Axle. Attach Axle Pin into 1x2 Beam Pin and Axle
Long Pin

## Slide 12
Flip-over sensor to attach remaining 1x2 Beam Hole and Axle
Insert Long Pin in Angle Sensor. Attach 4 Pin 3L into 3x5 Liftarm
Long Pin
Attach 3x5 Liftarm onto pins and flip-over
Attach remaining 3x5 Liftarm onto pins

## Slide 13
Completed Angle Sensor Mount

## Slide 14
Step B-2: Angle-to-Truss Connection
Gather 4 Friction Pins and 1 7-Beam from Step B-1, the Angle Sensor Mount from Step B-1, and Truss Sub-Assembly from Step A-5
Insert 2 Friction Pins at the ends of one of the 7-Beams. Insert 2 Friction Pins on the Sensor Mount
Attach 7-Beam to Sensor Mount. Then, Attach to the Truss Sub-Assembly
Repeat for other 7-Beam

## Slide 15
Completed Angle Sensor to Truss Sub-Assembly

## Slide 16
Step C: Base Sub-Assembly
Stuff to do:
Need those 90-deg hooking parts (don’t know name)
Step D: Pendulum Sub-Assembly
Step E: Cabling Channels Assembly
Step F: Motorized-Propeller Wiring
Step G: NXT Cable hook-ups