## Slide 1
Dynamixel XL-320 to LEGO NXT Connection
Last updated 06/11/19
Preamble: The LEGO NXT’s Port 4 is a RS-485 serial port. RS-485 operates at +/-12 Volts. However the Dynamixel XL-320 operates its serial lines on TTL (i.e. 0 to 5 Volt) levels. As such, a TTL-to-RS485 converter is used.
Four AA Battery pack
DROX TTL-to-485 converter
NXT Port 4
Common Ground

## Slide 2
Last updated 06/11/19
Step 1: 6 Volt Motor (Dynamixel XL-32) Voltage wiring
Datasheet of XL-320 shows pins connections.
http://emanual.robotis.com/docs/en/dxl/x/xl320/#control-table-of-eeprom-area
NB: left figure is from Top i.e. looking into the servo horn
BLK Jumper
RED Jumper
Not connected
Insert jumper wires into the XL-320’s Molex connector. Connect red jumper to battery 6v, connect black jumper to common ground.
Note: Work with XL-320 Right side connector.
Servo
Horn
+6V to XL-320 pin2
Battery GND to common GND
Common GND

## Slide 3
Last updated 06/11/19
Step 2: DROX to Dynamixel XL-320 (TTL) Wiring
DROX Pinout diagram https://www.droking.com/ttl-to-rs485-module-dc-3.0v-30v-rs485-to-ttl-mutual-conversion-hardware-automatic-flow-control-module-converter-module?search=ttl%20to%20rs485&description=true
DATA to TXD: YLW Jumper
DROX Vcc wire (RED)
To XL-320 DATA Pin 3 (BLU)
DROX GND wire (BLK)
Blue from DROX RXD connects to XL-320 Pin 3 (Data)
Black from DROX GND to breadboard common ground.
GNDs tied to Breadboard GND

## Slide 4
Last updated 06/11/19
Step 3: DROX to NXT Wiring (RS-485)
DROX (B-) to NXT (SCL Pin 5)
DROX (A+) to NXT (SDA Pin 6)
DROX (GND) to NXT (GND Pin 2)
Splice NXT cable
Connect YLW (SCL), BLU (SDA) and BLK (GND) wires into the DROX screw terminal from breadboard using jumper.
Connect GRN (+5v) to DROX red wire.
To DROX RS485 Ground
To DROX B-
To DROX A+
To DROX Vcc